## Slide 1: Application of boundary integral quadrature method to a circular torsion bar with an edge crack
Date: July 24, 2024
Time: 11:25~11:45
Place: Room 205,
Vancouver Convention Centre
Jia-Wei Lee, Yu-Sheng Hiesh & Jeng-Tzong Chen
Minisymposium 0803
Advance and application
of meshfree methods

## Slide 2
Tamkang University
Canada
Vancouver Convention Centre
TKU
Taiwan
Private university
We spent about 12 hours taking the airplane.

## Slide 3
Outline
Introduction
Problem statement
Present approach
Numerical results
Conclusions

## Slide 4
Outline
Introduction
Problem statement
Present approach
Numerical results
Conclusions

## Slide 5
Torsion Problem
Civil engineering
Mechanical engineering
Aerospace engineering
the twisting of an object due to an applied torque
https://upload.wikimedia.org/wikipedia/ commons/4/4f/Twisted_bar.png
Reinforced Concrete
steel construction
torsion buckling
shaft
https://www.abri.gov.tw/PeriodicalDetail.aspx? n=861&s=1786&key=70&isShowAll=false
screw
automobile drive shaft
flaps
rotary wing
https://www.apexflightacademy.com/ post/hang-kong-xiao-jiao-shi-left-turning-tendency
Architecture
machine element
aircraft
Motivation

## Slide 6: Literature Review
Torsion Problem containing cracks |  |  | 
1998 | 2005 | 2014 | 2019
J.T. Chen et al. | Y. B. Wang and Z. Z. Lu | A. Hassani and R. T. Faal | Y. T. Lee et al.
Used the dual boundary element to solve the cracked torsion bar. | Calculated the torsional rigidity and stress intensity factor for a cylinder with curvilinear cracks | Calculated the torsional rigidity and stress intensity factor with a circular cross-section containing multiple cracks. | Used the dual null-field BIEM to compute the torsional rigidity and stress intensity factor solve a circular bar containing multiple holes and/or cracks.

## Slide 7: Motivation
 | Null-field BIEM | Conventional BEM
Pros | Meshless Well-posed Free of boundary layer effect Exponential rate convergence Free of principal values | Arbitrary geometry
Cons | Only special geometry (circle or ellipse) | Need mesh generation in model preparation
We proposed the Meshfree BIEM that have both advantages of these two methods since 2021
Boundary
Nodes
Degenerate kernel
Fourier series
Boundary elements
Closed-form fundamental solution
Interpolation function

## Slide 8
Development of BIQM
Since 2021 |  | 2023 | 2024
Interior potential problem | Membrane free vibration problem | Steady state heat conduction problem | 
Exterior anti-plane problem | SH-wave scattering problem |  | 
Simply-connected domain |  | Multiply-connected domain | Degenerate boundary
Laplace equation | Helmholtz equation | Laplace equation | 
Singular integral (Adaptive exact solution) Nearly singular integral (Adaptive exact solution) Meshfree (Gaussian quadrature) |  | Singular integral (Adaptive exact solution) Nearly singular integral (Adaptive exact solution) Meshfree (Gaussian quadrature) Degenerate scale (CLEEF) Degenerate boundary (Dual BIEM) Singular integral on slit (Adaptive exact solution for slit) | 

## Slide 9
Outline
Introduction
Problem statement
Present approach
Numerical results
Conclusions

## Slide 10
Torsion problem containing an edge crack
Displacement fields
Boundary condition
is the shear modulus
is the angle of twist per unit length
Stress fields
Beltrami–Michell compatibility equation
Equilibrium equation
Governing equation
is the stress function

## Slide 11
Outline
Introduction
Problem statement
Present approach
Numerical results
Conclusions

## Slide 12
in the complementary domain
in the domain
on the boundary
Basic solution of Laplace equation
Boundary integral equation

## Slide 13
x
s
x
s
CPV (Cauchy)
(Kisu, 1988)
Who is responsible for the discontinuity of the
double-layer potential? (boundary, kernel or density?)
p(x) jump from De to Di.
Gauss’ theorem
Residue Theorem
山不轉。路轉。
山不轉。路不轉。人轉。
discontinuity
邊界密度函數的解析延拓。
(Taylor expansion)
Degenerate kernel
Bump contour

## Slide 14
w=() &
Skillful calculation of singular integral
Adaptive exact solution
computation of solid angle is free
Discontinuous
Continuous
To enforce the smoothness and continuity of potential and its normal flux across the boundary, we introduce the adaptive exact solution.

## Slide 15
Integral equation to algebraic equation
Boundary node points
Gaussian points
Gaussian quadrature
Parametric representation for each boundary
IE -> AE

## Slide 16
Dual BIE for the degenerate boundary
UT
LM
In addition, the dual BIE is also required for present problem.

## Slide 17
Adaptive exact solution for the degenerate boundary
When a collocation point is located on the degenerate boundary,
the singularities may occur in both upside and downside of the degenerate boundary at the same time.
Therefore, the above adaptive exact solution is not suitable.

## Slide 18
Adaptive exact solution for the degenerate boundary
According to the continuous conditions across the boundary, we have four continuous equations for a collocation point located on the degenerate boundary.

## Slide 19
Adaptive exact solution for the degenerate boundary
E
We employ the exterior harmonic basis of the elliptical coordinates to derive the adaptive exact solution.

## Slide 20
A self-regularized approach
Introduce the self-regularized approach
UT
LM
UT
UT
promoting the rank of the deficient matrix
for an degenerate boundary
singular value decomposition
algebraic equation
rearrange

## Slide 21
Outline
Introduction
Problem statement
Present approach
Numerical results
Conclusions

## Slide 22
A circular cross-section with a radial edge crack
Ratio of torsional rigidity , () |  |  |  | 
 | BIQM + self-regularized approach | Dual BIQM | Conventional dual BEM (No. of boundary element) | Analytical solution Lebedev et al.
0.5 |  |  |  | 
0.6 |  |  |  | 
0.7 |  |  |  | 
0.8 |  |  |  | 
0.9 |  |  |  | 
1 |  |  |  | 
 | BIQM + self-regularized approach | Dual BIQM |  | Analytical solution Lebedev et al.
0.5 |  |  |  | 
0.6 |  |  |  | 
0.7 |  |  |  | 
0.8 |  |  |  | 
0.9 |  |  |  | 
1 |  |  |  | 
References：
N. N. Lebedev, I. P. Skalskaya and Y. S. Uflyand, Worked problems in applied mathematics, Dover, New York, 1965.
Torsional rigidity

## Slide 23
A circular cross-section with a radial edge crack
Stress intensity factor
Ratio of stress intensity factor , () |  |  |  | 
 | BIQM + self-regularized approach | Dual BIQM | Hassani and Faal | Wang
0.1 |  |  | 0.9566 | 0.9591
0.2 |  |  | 0.9276 | 0.9280
0.3 |  |  | 0.9090 | 0.9088
0.4 |  |  | 0.8979 | 0.8973
0.5 |  |  | 0.8920 | 0.8913
0.6 |  |  | 0.8892 | 0.8883
0.7 |  |  | 0.8872 | 0.8864
0.8 |  |  | 0.8835 | 0.8830
0.9 |  |  | 0.8752 | 0.8777
1 |  |  | NA. | NA.
 | BIQM + self-regularized approach | Dual BIQM | Hassani and Faal | Wang
0.1 |  |  | 0.9566 | 0.9591
0.2 |  |  | 0.9276 | 0.9280
0.3 |  |  | 0.9090 | 0.9088
0.4 |  |  | 0.8979 | 0.8973
0.5 |  |  | 0.8920 | 0.8913
0.6 |  |  | 0.8892 | 0.8883
0.7 |  |  | 0.8872 | 0.8864
0.8 |  |  | 0.8835 | 0.8830
0.9 |  |  | 0.8752 | 0.8777
1 |  |  | NA. | NA.
References：
A. Hassani and R. T. Faal, Saint-Venant torsion of orthotropic bars with a circular cross-section containing multiple cracks, Mathematics and Mechanics of Solids, Vol. 21, pp. 1-17, 2014.
Y. Wang, Torsion of a thick-walled cylinder with an external crack: boundary collocation method, Theoretical and Applied Fracture Mechanics, Vol. 14, pp. 267-273, 1990.

## Slide 24
A circular cross-section with a slant edge crack
References：
J. T. Chen, K. H. Chen and W. Yeih, Dual boundary element analysis for cracked bars under torsion, Engineering Computations, Vol. 15 (6), pp. 732-749, 1998.
A. Hassani and R. T. Faal, Saint-Venant torsion of orthotropic bars with a circular cross-section containing multiple cracks, Mathematics and Mechanics of Solids, Vol. 21, pp. 1-17, 2014.
Torsional rigidity

## Slide 25
A circular cross-section with a slant edge crack
References：
A. Hassani and R. T. Faal, Saint-Venant torsion of orthotropic bars with a circular cross-section containing multiple cracks, Mathematics and Mechanics of Solids, Vol. 21, pp. 1-17, 2014.
Torsional rigidity
Ratio of torsional rigidity, , () |  |  | 
 | BIQM + self-regularized approach | Dual BIQM | Conventional dual BEM (No. of boundary element)
0.5 |  |  | 
0.6 |  |  | 
0.7 |  |  | 
0.8 |  |  | 
0.9 |  |  | 
1 |  |  | 
 | BIQM + self-regularized approach | Dual BIQM | 
0.5 |  |  | 
0.6 |  |  | 
0.7 |  |  | 
0.8 |  |  | 
0.9 |  |  | 
1 |  |  | 

## Slide 26
A circular cross-section with a slant edge crack
References：
A. Hassani and R. T. Faal, Saint-Venant torsion of orthotropic bars with a circular cross-section containing multiple cracks, Mathematics and Mechanics of Solids, Vol. 21, pp. 1-17, 2014.
Stress intensity factor
Ratio of stress intensity factor , () |  | 
 | BIQM + self-regularized approach | Dual BIQM
0.1 |  | 
0.2 |  | 
0.3 |  | 
0.4 |  | 
0.5 |  | 
0.6 |  | 
0.7 |  | 
0.8 |  | 
0.9 |  | 
1 |  | 
 | BIQM + self-regularized approach | Dual BIQM
0.1 |  | 
0.2 |  | 
0.3 |  | 
0.4 |  | 
0.5 |  | 
0.6 |  | 
0.7 |  | 
0.8 |  | 
0.9 |  | 
1 |  | 

## Slide 27
A circular cross-section with a slant edge crack
References：
A. Hassani and R. T. Faal, Saint-Venant torsion of orthotropic bars with a circular cross-section containing multiple cracks, Mathematics and Mechanics of Solids, Vol. 21, pp. 1-17, 2014.
Torsional rigidity
Stress intensity factor

## Slide 28
elliptical cross-section with double radial edge cracks
References：
N. N. Lebedev, I. P. Skalskaya and Y. S. Uflyand, Worked problems in applied mathematics, Dover, New York, 1965.
Ratio of torsional rigidity, , () |  |  |  |  | 
 |  | BIQM + self-regularized approach | Dual BIQM | Conventional dual BEM (No. of boundary element) | Analytical solution Lebedev et al.
 |  |  |  | 0.8251 | 
 |  | BIQM + self-regularized approach | Dual BIQM |  | Analytical solution Lebedev et al.
Ratio of stress intensity factor, , () |  |  | 
 |  | BIQM + self-regularized approach | Dual BIQM
 |  | BIQM + self-regularized approach | Dual BIQM

## Slide 29
Outline
Introduction
Problem statement
Present approach
Numerical results
Conclusions

## Slide 30
Conclusions
1. After introducing the adaptive exact solution and Gaussian quadrature, the BIQM is a meshless method.
2. To solve the rank-deficient problem arising from a degenerate boundary in the BIQM, we used not only the dual BIE but also the self-regularized approach.
UT
LM
Dual BIE
UT
UT
Aelf-regularized approach
(only singular BIE)

## Slide 31
Conclusions
4. For the slant case, it is found some difference between the present results and the results of reference.
3. For the torsional rigidities, the results of BIQM is more accurate than those of conventional dual BEM.
Ratio of torsional rigidity, , () |  |  |  |  | 
 |  | BIQM + self-regularized approach | Dual BIQM | Conventional dual BEM (No. of boundary element) | Analytical solution Lebedev et al.
 |  |  |  | 0.8251 | 
 |  | BIQM + self-regularized approach | Dual BIQM |  | Analytical solution Lebedev et al.

## Slide 32
Related papers
J. W. Lee*, H. W. Yang and J. T. Chen, 2023, ASME Journal of Heat and Mass Transfer, Vol. 145 (11), p.110901.
J. W. Lee*, H. W. Yang and J. T. Chen, 2024, Engineering Analysis with Boundary Elements, Vol. 165, 105798.
if anyone has interest on the BIQM, two papers are now available.
The pdf file is upon your request.

## Slide 33: The end
Thanks for your kind attentions

## Slide 34
Conclusions
Double degeneracy
Outer boundary
Ellipse
Degenerate scale
CLEEF & Dual BIE
Inner boundary
Slit
Degenerate boundary
Dual BIE
Degenerate scale is dominated by the outer boundary instead of the inner boundary.
The dual BIE is the well-posed model for dealing with all degenerate problems.

## Slide 35
Related papers
J. W. Lee*, H. W. Yang and J. T. Chen, 2023, ASME Journal of Heat and Mass Transfer, Vol. 145 (11), p.110901.
J. H. Kao, J. W. Lee*, J. Y. Young and J. T. Chen, 2023, Numerical Heat Transfer, Part B: Fundamentals, accepted.
J. W. Lee*, H. W. Yang and J. T. Chen, 2024, Engineering Analysis with Boundary Elements, Vol. 165, 105798.
J. H. Kao, C. Y. Yang, J. W. Lee*, J. T. Chen, 2024, International Journal of Heat and Mass Transfer, Accepted.
If anyone has interesting to our work. There are four related papers can be found.
The pdf file is upon your request.

## Slide 36
Degenerate scale
2D Laplace problem
BEM/BIEM
No solution or non-unique
694
The value of degenerate scale in the numerical result can be predicted by using the analytical derivation.
Dirichlet BC

## Slide 37
Method 1 | Method 2
Hypersingular boundary integral equation | CLEEF (UT or LM)
Treatments for degenerate scale
(
=CLEEF point

## Slide 38
The meshfree boundary integral method was successfully applied to solve the two-dimensional steady-state heat conduction problem of heat exchanger tubes containing slits.
The generation of the mesh on the boundary was not required in the model preparation.
The proper local exact solution for a problem containing a degenerate boundary was constructed by using the harmonic basis in elliptical coordinates.
The CLEEF idea can be employed to effectively suppress the numerical instability due to a degenerate scale.
Conclusions

## Slide 39
Heat transfer Problem: Conduction shape factor
Fellow of the American Academy of Arts and Sciences (1918)
Perkin Medal (1928)
Nobel Prize in Chemistry (1932)
Franklin Medal (1934)
Faraday Medal (1944)
Irving Langmuir
1913年 | 1961年
Convection and radiation of heat | Steady state temperature distribution and heat flow in prismatic bars with isothermal boundary conditions
Irving Langmuir | M.J.Balcerzak、S.Raynor
Trans. Am. Electrochem Soc. 23,299–332 | International Journal of Heat and Mass Transfer, 3, 113-125
He was the first to propose the concept of conduction shape factor. | Conformal mapping was used to calculate the temperature distribution, and exact solution for the conduction shape factor was derived.

## Slide 40: Motivation
 | Null-field BIEM | Conventional BEM
Pros | Meshless Well-posed Free of boundary layer effect Exponential rate convergence Free of principal values | Arbitrary geometry
Cons | Only special any (circle or ellipse) | Need mesh generation in model preparation
To develop a BIEM with Meshfree & for Arbitrary Geometry
Boundary
Nodes
Degenerate kernel
Fourier series
Boundary elements
Closed-form fundamental solution
Interpolation function

## Slide 41
Development of meshfree BIEM
Since 2021 |  | 2023
Interior potential problem | Membrane free vibration problem | Steady state heat conduction problem
Exterior anti-plane problem | SH-wave scattering problem | 
Simply-connected domain |  | Multiply-connected domain
Laplace equation | Helmholtz equation | Laplace equation
Singular integral (Adaptive exact solution) Nearly singular integral (Adaptive exact solution) Meshfree (Gaussian quadrature) |  | Singular integral (Adaptive exact solution) Nearly singular integral (Adaptive exact solution) Meshfree (Gaussian quadrature) Degenerate scale (CHEEF) Degenerate boundary (Dual BIEM) Singular integral on slit (Adaptive exact solution for slit)

## Slide 42
An elliptical tube containing a focal slit
Governing equation: Laplace equation
Boundary condition
Constant temperature
temperature field
outer boundary temperature (unit: K) inner boundary temperature (unit: K) outer boundary inner boundary

## Slide 43
in the complementary domain
in the domain
on the boundary
Basic solution of Laplace equation
Boundary integral equation

## Slide 44
w=() &
by using the
shape functions
Skillful calculation of singular integral
Adaptive exact solution
computation of solid angle is free

## Slide 45
Auxiliary solution
Subtract
Adaptive exact solution

## Slide 46
satisfies the 2D Laplace equation
When
Adaptive exact solution

## Slide 47
Adaptive exact solution for the degenerate boundary
E
Harmonic basis for the exterior problem

## Slide 48
Adaptive exact solution for the degenerate boundary

## Slide 49
Single slit and multiple slits
Elliptical tube containing a focal slit
Elliptical tube containing 3 radial slits
a=5
b=4
a=5
b=4
l=1

## Slide 50
Contour plots of the temperature field
Elliptical tube containing a focal slit
Elliptical tube containing 3 radial slits
Meshfree BIEM
Dual BEM
Meshfree BIEM
Dual BEM

## Slide 51
CSF and degenerate scale
Elliptical tube containing a focal slit
Elliptical tube containing 3 radial slits

## Slide 52
The meshfree boundary integral method was successfully applied to solve the two-dimensional steady-state heat conduction problem of heat exchanger tubes containing slits.
The generation of the mesh on the boundary was not required in the model preparation.
The proper local exact solution for a problem containing a degenerate boundary was constructed by using the harmonic basis in elliptical coordinates.
Conclusions

## Slide 53
This work also numerically verified that all the cases suffered the problem of degenerate scale due to the logarithmic kernel and corresponding size of the outer boundary.
The CLEEF idea can be employed to effectively suppress the numerical instability due to a degenerate scale.
Double degeneracy of not only the degenerate scale of outer boundary but also the degenerate boundary of inner slit, were solved at the same time by using regularization techniques and dual equations, respectively.
Conclusions

## Slide 54
Deal with nearly singular integral by adaptive exact solution
Adaptive exact solution
Subtract
out of domain
Boundary layer effect due to the nearly singular

## Slide 55
Dual boundary integral equation
BIEM/BEM for solving engineering problem
2D Laplace and Helmholtz equations
seepage
free vibration
anti-plane shear
wave scattering
Mesh reduction and efficient

## Slide 56
Null-field formulation
Null-field BIEM in NTOU/MSV since 2003
Fundamental solution
Degenerate kernel
Boundary density
Fourier series
a
Five advantages
Meshless
Well-posed
Free of boundary layer effect
Exponential rate convergence
Free of principal values

## Slide 57
Cross-section | Case 1 | 
 | Without the treatment of boundary layer effect | With the treatment of boundary layer effect
a=1
b=3
Contour plots of temperature fields

## Slide 58
Cross-section | Case 2 | 
 | Without the treatment of boundary layer effect | With the treatment of boundary layer effect
a=1
b=3
Contour plots of temperature fields

## Slide 59
Convergence of CSF
=4
=5
=6
=6